Electrical Requirements

AC Requirements

Pull four (4) 12 gauge wires from the motor side of the recessed box to the touch pad location.  Pull a hot, a neutral and an unbroken green ground from the panel to the touch pad location.  The power source should be on a 20 amp dedicated GFCI breaker. Follow all national and local codes regarding wire size, grounding and connectors.

#8 AWG solid copper bond wire must be provided for grounding the PowerTouch® System.  This bonding wire will be attached to the PowerTouch® frame.

NOTE:  Bonding wire should be at both ends of the box.

# Touch pad location

A ¾” conduit needs to be connected from the motor side of the recessed housing to the touch pad location.  The ¾”conduit going into the recessed box should junction into a standard J-Box.  The touch pad location must be located in full view of the pool, at least five (5) feet above ground level.

Parts Required

(1) – Double gang J-Box (at touch pad location)

(1) – ¾” J-box (at cover housing)

(3) – 12 AWG Wires from the Power Panel to touch pad location

(4) – 12 AWG Wires from housing to touch pad location

#8 bonding wire (from pool)

# Text boxes

Touch Pad location

Motor side of housing

¾” conduit

to J-Box

20 amp

GFCI

Three (3) #12 AWG Wires

AC/Power

Four (4) #12 AWG Wire

Double gang j-box

Keep five feet – (5’) above ground level

Pool Cover

Motor